## Slide 1
SPECIFICATIONS
FEATURES
Front and rear access, 3-seconds module disassembly with magnetic tool
2.8V&3.8V PCB design,based on SMD, can easily reach 10000nits,only need 450W/㎡
Module applies hard connection without flat cables, reducing failure rate while mproving stability
Aluminum profile cabinet owns high precision, ensuring the flatness of whole screen
Module is corner and flat screen 2 in 1 design, can make L shape corner cabinets
Product Model | GPO3.9 | GPO4.8 | GPO5.2 | GPO6.25 | GPO7.8 | GPO10.4
Pixel Pitch(mm) | 3.91 | 4.81 | 5.2 | 6.25 | 7.82 | 10.4
LED Type | SMD |  |  |  |  | 
Scan method | 1/8 scan | 1/7 scan | 1/6 scan | 1/5 scan | 1/4 scan | 1/2 scan
Brightness(cd/m2) | ≥5000 (8000-10000) | ≥5500 (8000-10000) | ≥6000 (8000-10000) | ≥6000 (8000-10000) | ≥6000 (8000-10000) | ≥6500 (8000-10000)
Refresh Rate(Hz) | ≥ 1920Hz（3840HzOptional) |  |  |  |  | 
Power Consumption(Max/Ave) (W/m2) | 800/270 | 800/270 | 550/185 | 500/175 | 500/175 | 500/175
Module Resolution(px) | 128 x 64 | 104 x 52 | 96 x 48 | 80 x 40 | 64 x 32 | 48 x 24
Module Size(mm) | 500x250 |  |  |  |  | 
Panel Resolution(px) | 256 x 256 | 208 x 208 | 192 x 192 | 160 x 160 | 128 x 128 | 96 x 96
Panel Size(mm) | 1000 x 1000 x 73mm (Optional) |  |  |  |  | 
Weight(kg/m2) | 24.5 |  |  |  |  | 
IP Rating(Front/Rear) | IP67/IP65 |  |  |  |  | 
Gray Scale(Bit) | 16 |  |  |  |  | 
Maintenance | Front&Rear |  |  |  |  | 
Operating Temperature/Humidity(°C/RH) | -20-65 10〜90% |  |  |  |  | 
GPO Series
GPO(P3.9/P4.8/P5.2/P6.25/P7.8/P10.4)