## Slide 1
SPECIFICATIONS
Product | P1.82 | P2 | P2.5 | P3.07 | P4
Pitch | 1.82mm | 2mm | 2.5mm | 3.07mm | 4mm
Resol ution(dots) | 352*1056 | 320*960 | 256*768 | 208*624 | 160*480
LED Type | SMD1515 |  | SMD2121 |  | 
Brightness | 1000nits |  | 1200nits |  | 
Module Size | 320*160mm |  |  |  | 
Total Poster Size | W655mm*H1936mm*T45mm |  |  |  | 
LED Size | W640*H1920mm |  |  |  | 
Material | Acrylic + Aluminum |  |  |  | 
Weight | 35 kg/pcs |  |  |  | 
Control Method | 4G/Wifi/Ethernet+Cloud Cluster Control+Mobile App |  |  |  | 
Protection Level | IP40 |  |  |  | 
Cabinet Maintenance | Front &Rear Service |  |  |  | 
Max Power Consumption | 700W |  |  |  | 
Average Power Consumption | 250W |  |  |  | 
Refresh Rate (Hz) | 2880-3840HZ |  |  |  | 
Grey Scale | 16 bit |  |  |  | 
Viewing Angle | H160°, V160° |  |  |  | 
Voltage | AC100~240V(50-63Hz) |  |  |  | 
Working Temperature | -40°C-+70°C |  |  |  | 
Working Humidity | 10%-90%RH |  |  |  | 
Color Temperature | 6500-9500K |  |  |  | 
Brightness Sensor | 0-255 level automatic adjustment, optional |  |  |  | 
Contrast Ratio | 4000:01:00 |  |  |  | 
Certifications | EMC/CE/ROHS/CCC/FCC/ISO |  |  |  | 
FEATURES
Multiple installation ways: hanging, wall-mounting, base-standing, bracket standing and creative installation
High brightness, high refresh rate, 160° viewing angle, a much better replacement of LCD screen
Can be controlled by mobile phone/computer/Wi-Fi /USB connection
Better replacement of traditional roll screen
Gposter Series
Gposter(P1.8/P2/P2.5/P3.07/P4

## Slide 2
SPECIFICATIONS
 | Indoor |  | Outdoor |  | 
Product | P1.875 | P2 | P2.5 | P3 | P4
Pitch | 1.875mm | 2mm | 2.5mm | 3mm | 4mm
Resol ution(dots) | 512*1024 | 480*960 | 384*768 | 320*640 | 240*480
LED Type | SMD1515 |  | SMD1921 |  | 
Brightness | 1000nits | 1000nits | 3500nits | 4500nits | 5500nits
Module Size | 240*240mm |  | 320*160mm |  | 
Total Poster Size | W1140*H2100*T210mm |  |  |  | 
LED Size | W960*H1920mm (Customizable) |  |  |  | 
Bottom Wheel | H27.5mm (Dismountable, optional) |  |  |  | 
Material | Tempered Glass + Galvanized Aluminum |  |  |  | 
Weight | 70kg/pcs |  |  |  | 
Control Method | 3G/4G/Wifi+Cloud Cluster Control+Mobile App |  |  |  | 
Protection Level | IP65 |  |  |  | 
Cabinet Maintenance | Front&Rear Service |  |  |  | 
Max Power Consumption | 1200W |  | 1800W |  | 
Average Power Consumption | 400W |  | 600W |  | 
Refresh Rate (Hz) | 2880-3840HZ |  |  |  | 
Grey Scale | 16 bit |  |  |  | 
Viewing Angle | H160°, V160° |  | H160°, V140° |  | 
Voltage | AC100~240V(50-63Hz) |  |  |  | 
Working Temperature | -30°C - +80°C |  |  |  | 
Working Humidity | 10%-90%RH |  |  |  | 
ColorTemperature | 6500-9500K |  |  |  | 
Brightness Sensor | 0-255 level automatic adjustment, optional |  |  |  | 
Power Control | Remote power control, optional |  |  |  | 
Monitoring | HD camera, optional |  |  |  | 
Sound System | Power consumption 10-30W, optional |  |  |  | 
Enviroment Detection | Temperature/Humidity/PM2.5, optional |  |  |  | 
Certifications | EMC/CE/ROHS/CCC/FCC/ISO |  |  |  | 
FEATURES
Multiple installation ways: floor-standing,pillar-mounting, hanging,etc
Can be controlled by mobile phone /computer/Wi-Fi/3G/4G/Cloud-clu stered-control
Precision advertising with face recognition function
Enough space for inside sound system
Remote control for the power switch
Brightness sensor for automatic brightness adjustment
Optional bottom wheels
Compatible with HD camera for monitoring
Gposter Series
Gposter(P1.8/P2/P2.5/P3.07/P4)